| Institution: Faculty of Chemistry and Chemical Engineering Research Center for Computer Aided Design in Chemical Engineering Design and testing systems laboratory for modeling, simulation and control of chemical processes and for development of e-learning techniques Address: Arany Janos Street , no 11, room 55 Tel: 0264 593833 Contact person: Assoc. Prof. PhD. Eng. Cristea Vasile Mircea e-mail: mcristea@chem.ubbcluj.ro |  |
| --- | --- |
| Equipment: Automatic Multi-Process Control System UNIPRO/EV (Flowrate, level, temperature and speed) |
| Characteristics and performances: Highly flexible and modular system for studying the control of industrial processes. It has been designed to include all systems, devices and instruments typical of industrial processes into a single-structure. The system, includes: physical process transducers actuators control device computerized supervision system Date of purchasing: 2008 |
| Applications: Development of methods for the description of typical physical and chemical processes Testing components and equipment for measuring, monitoring and control Testing and developing computer, interfaces and devices for data transmission Testing and developing microprocessor digital control systems Development of computer based monitoring and measurement systems Testing Proportional control, Proportional+integral control, Proportional+derivative control, Proportional+integral+derivative control, Cascade control Controller tuning Development of computer based control algorithms and testing their performance for industrial implementation |
| Offer addressed to potential internal and external users: The experimental facilities will be available correlated to the schedule of the teaching program performed in the laboratory Costs will be agreed according to the custom’s particular experimenting program |
| Funding source: Funds for the development of didactic laboratories |
| Estimated value: 30000 EUR |