| Institution: Faculty of Chemistry and Chemical Engineering Departament of Chemical Engineering Address: Arany Janos Street , no 11, ground floor/room 208 Tel: 0264 593833 Contact person: Lecture PhD. Eng. Reka Barabas e-mail: breka@chem.ubbcluj.ro |  |
| --- | --- |
| Equipment: ALICAT Mass flow controllers |
| Characteristics and performances: Mass Flow: 0 la 250 SLPM Volumetric Flow: 0 la 250 LPM Pressure (PSIA): <145 psig Temperature (° Celsius or ° Fahrenheit): -10 pana la +50 grd C Pressure and temperature measurements are taken and displayed in the same unit, (MC, MCP & MCR Series) Mass flow controllers can be set by user to control pressure RS-232 output of all measured parameters 30-Gas Select on all units to reduce inventory costs Control range from 1% to 100% of full scale flow Date of purchasing: 2009 |
| Applications: Ideal instrument for a variety of processes, including: vacuum coating, process automation, semiconductor processing, etc. |
| Offer addressed to potential internal and external users: The price will be establish from user to user |
| Funding source: Funds for the development of didactic laboratories |
| Estimated value: 750 EUR |