| Institution: Faculty of Chemistry and Chemical Engineering The The Insitute for Interdisciplinary Experimental Research Centre of biomaterials Address: Treboniu Laurian Street, No. 34, level II/202 Tel: 0264 454554 Contact person: Lecture PhD. Eng. Reka Barabas e-mail: breka@chem.ubbcluj.ro |  |
| --- | --- |
| Equipment: Counter Coulter SALD-7101 Shimadzu |
| Characteristics and performances: Measurement domain: 0,015…500 (m Measurement method: laser diffraction Optical system: LED Laser=405 nm Photo-detector: 81 elements 75 elements for superior scatter 5 for inferior scatter Cell for samples: dosing cell of pirex glass and etilen-tetraflouride-12 ml flow cell of melted quartz, stainless stell and etilen-tetraflouride Auto-sampler: dispersion is made with the help of ultrasounds Samples bath: 280 cm3 Mechanical stirrer with blades and adjusted speed Pomp for liquids: radially pomp 1600 ml/min Materials: stainless steel, etilen-tetraflouride, popliacetal resin, caoutchouc nitril and viton Date of purchasing: 2007 |
| Applications: Offers information about particle size distributions from suspensions and emulsions |
| Offer addressed to potential internal and external users: The price will be establish from user to user |
| Funding source: Funds for the development of didactic laboratories |
| Estimated value: 35000 EUR |