| Institution: Faculty of Chemistry and Chemical Engineering Didactic and Research Laboratory for Transfer Phenomena in Chemical Engineering Address: Arany Janos Street , no 11, room 208 Tel: 0264 593833 Contact person: Assoc. Prof. PhD. Eng. Adina Lucreţia GHIRIŞAN e-mail: ghirisan@chem.ubbcluj.ro |  |
| --- | --- |
| Equipment: BOKELA FILTRATEST |
| Characteristics and performances: Filtration cell with a capacity of 0.5 L and with double chamber system Filtrate hopper with a filtration surface with area of 20 cm2 Volume flow measuring device VSM-02 Mechanical pressure gauge (max. 10 bar) and prevision pressure reducer Balance METTLER TOLEDO Laptop with software for on-line measurement, registration and interpretation Date of purchasing: 2008 |
| Applications: Pressure filtration tests of different suspensions and disperse systems from industrial processes and wastewater treatments Characterisation of filtration cake (filtration constants and specific resistances) Design of industrial equipments |
| Offer addressed to potential internal and external users: The experimental facilities will be available correlated to the schedule of the teaching program performed in the laboratory Costs will be agreed according to the custom’s particular experimenting program |
| Funding source: Grants for teaching laboratory |
| Estimated value: 35000 EUR |