| Institution: Faculty of Chemistry and Chemical Engineering Department of Chemical Engineering and Material Science Chemical Reaction Engineering (CRE) Address: 11, Arany Janos Str, room 13 Tel: 0264 593833 Contact person: Assoc. Prof.PhD.Eng. Cormos Calin e-mail: cormos@chem.ubbcluj.ro |  |
| --- | --- |
| Equipment: Chemical reactor kit (ElettronicaVeneta) |
| Characteristics and performances: Chemical reactor kit (manufacturing company ElettronicaVeneta, Italy) is supplied with a common platform for various chemical reactors to be analysed (batch reactor, plug flow reactor - PFR, continuous stirred tank reactor - CSTR, serie of CSTR reactors). The platform is equiped with reactant tanks (2 pieces), peristaltic dosing pumps (2 pieces) with digital display, controller of the stirrer (3 pieces), heating bath and warm water circulator and possibilities to process parameters monitoring (conductivity and temperature). The kit is also supplied with on-line monitoring software. Technical details: Reactant tank capacity 2 x 5 liter Dosing pump flow 0 – 95 ml/min. Stirrer controler 0 – 400 rpm Batch reactor volume 0.75 liter PFR reactor volume 0.5 liter CSTR reactor volume 0.75 liter Operational thermal mode adiabatic, isothermal, programed On-line monitoring Software “Pilot for Windows” Date of purchasing: 2009 |
| Applications: Chemical reactor kit can be used for analysing the operation regime of different chemical reactors (batch reactor, plug flow reactor - PFR, continuous stirred tank reactor - CSTR, serie of CSTR reactors), mass balance for chemical reactors, kinetic and flow studies (e.g. residence time distribution). |
| Offer addressed to potential internal and external users: Not the case |
| Funding source: Funds for the development of didactic laboratories |
| Estimated value: 40000 RON |