| Institution: Faculty of Chemistry and Chemical Engineering Depertent of Chemical Engineering Address: Arany Janos Street , no 11, ground floor/room 208 Tel: 0264-593-833 Contact person: Lecture PhD. Eng. Reka Barabas e-mail: breka@chem.ubbcluj.ro |  |
| --- | --- |
| Equipment: Mini Spray Dryer B-290 |
| Characteristics and performances: Power Rating: 2900 W Voltage: 200/230 V, 50–60 Hz Evaporative Capacity: 1.0 l/hr H2O, higher for organic solvents Air Flow: Max. of 35 cu. m./hr Max. Temperature Input: 220 °C Heating Capacity: 2300 W Interface: Serial port RS-232 for all parameters Spray Gas: Compressed air or nitrogen, 200–1000 l/hr, 5–8 bar Nozzle Diameter: 0.7 mm Standard Possible particle diameter range: 1–25 μm Dimensions : L xWxH 60 x 50 x 110 cm Weight: 48 kg Date of purchasing: 2009 |
| Applications: Mini Spray Dryer B-290 make it possible to obtain powder directly from a solution but many other processes can also be completed in a single stage: Modification of particle size Agglomeration of nanoparticles Drying suspensions Particle coating Manufacture of microcapsules |
| Offer addressed to potential internal and external users: The price will be establish from user to user |
| Funding source: Funds for the development of didactic laboratories |
| Estimated value: 23300 EUR |