| Institution: Faculty of Chemistry and Chemical Engineering Department of Science and Engineering Oxide Materials and Nanomaterials Laboratory of design, obtaining and characterization ceramics Address: 11, Arany Janos Str, room 10 Tel: 0264 593833 Contact person: Assoc prof. Dr. Ing. Gorea Maria e-mail: mgorea@chem.ubbcluj.ro |  |
| --- | --- |
| Equipment: Horizontal dilatometer L75Hx1400 (Linseis) Water cooler Computer and printer |
| Characteristics and performances: Temperature Range: 20 ˚C to 1400 ˚C Heating rate: 0.1 la 50 ˚C/min Tested sample size: diameter - max 6 mm; lenght – to 50 mm Furnace cooling: air; Furnace Atmospere: air; Heating Element: Kanthal; Measuring Standard: Al2O3; Repeatability: ± 150 nm; Accuracy: ± 1 % (full scale); Date of purchasing: 2008 |
| Applications: Dilatometer measures the change in sample lenght during the thermal treatment. Relative change of lenght; Coefficient of linear expansion; Tranformation point; Sample Shrinking. Storing the data; Evaluation of measurements; |
| Offer addressed to potential internal and external users: The experimental facilities will be available correlated to the schedule of the teaching program performed in the laboratory Costs will be agreed according to the custom’s particular experimenting program |
| Funding source: Funds for the development of didactic laboratories |
| Estimated value: 109301 RON |