| Place: Faculty of Chemistry and Chemical Engineering Computer Aided Chemical Engineering Research Center Laboratory for the study of gas-solid heterogeneous processes (SPEC) Address: Str. Arany Janos, nr. 11, sala nr. 7 Tel: 0264 593833 Contact: Lect. Dr. Ing. Botar-Jid Claudiu Cristian e-mail: cbotar@chem.ubbcluj.ro |  |
| --- | --- |
| Equipment name: Quardupole Mass Spectrometer (KNK-Q12-000, MS 012 for GC EI, 1204 Mass Range 1 TMP) Tubular Furnace Computers Specific softwares |
| Characteristics: • Quardupole Mass Spectrometer – On-line aquisition Ionization source by Electron Impact (EI) Quadrupole analyser with pre-filters Complete automatic and manual tune modes Full scan and Single Ion Monitoring (SIM) modes of mass analysis Positive ion detection in EI mode Variable and Programable EI ionization voltage Variable and programable EI filament current Photon ion conversion detectionsystem for positive ions Vacuum system composed by one hybrid air cooled 200 l/s turbomoleculardrag pump roughed by a 5m3/h oil sealed rotary vane pump. Full automatic vacuum control system Interfata GC/MS pentru sisteme capilare si semicapilare Mass range from 4 to 1024 amu Scan rate: programable up to 33,000 amu/sec Interface for LC MS operation Aquisition date: 2008 Tubular furnace; RS232 interface PID controller Temperature range 0-1200 (C |
| Applications and use: Gas-solid heterogeneous processes, general gas analysis |
| External users (use and costs): Availability according to the laboratory activities plan Costs exploitation will be established acordingly to the market costs |
| Financial support for apparatus acqisition: Contract Nr. CNCSIS 1322, Rompetrol sponsorship founds. |
| Value: 60000 EUR |